Test Documentation For CAN bus

- Initial testing was done using demo code provided by the application note on the MSCAN for HSC12
- First test was compiling the code
  - This failed, extensive syntax errors and logical errors were present in the code
  - After debug and code rewrite, we were able to compile our code
- Second test was done using the LCD module that we had already set up
  - A can message was sent using the adjusted demo code, and when the message was received by our interrupt function, code outputted the received CAN message to the LCD screen as a string.
  - This test was a partial success, the message output to the LCD screen, however as we didn't format the message in a string format, the successful message was followed by a number of bytes of garbage
    - This was followed up by using the debugger to see what was the actual CAN message received, and confirm there was no actual garbage in the can message
- At this stage, code was written to generate message node ID's, as well as masks to fit and accept CAN messages according to the protocol our teams determined previously
  - The first test for this change was to send a message to a single ID, and confirm receipt
    - This was successful
  - The following test was to send to a single ID that our node should NOT accept, and confirm the message didn't get past the filter
    - This was unsuccessful, due to an error in the macro converting from the node ID into the correct mask which would only care about the specific bit in question
      - This was troubleshot, and the macro was corrected to properly invert and shift the ID into the correct position for the mask
    - Then this test was repeated, and was successful
  - The next test confirmed that a broadcast sent to all nodes was properly received by our node
    - This was successful
  - Then we tested a multicast sent to nodes including our node was properly received, and a multicast sent to nodes excluding our node was not received
    - This was successful
- At this stage we considered our CAN api functions to be successful, and we moved on with our project implementation